## Slide 1
SWPPP INTRODUCTION
For the Boots on the Ground
January 2022

## Slide 2: SWPPP Introduction
Goals of this section:
Be able to describe the purpose of a SWPPP;
Name the parts of a SWPPP; and
Know what makes a good SWPPP.

## Slide 3
What Elements Are Required in a SWPPP?
• Cover/title page
• Project and SWPPP contact information
• Site and activity description, including a site map
• Identification of potential pollutant sources
• Description of controls to reduce pollutants
• Maintenance/inspection procedures
• Records of inspections & maintenance of BMPs
• SWPPP amendments
• SWPPP certification
First and foremost, your SWPPP must be developed and implemented consistent with all permits.

## Slide 4: What is an Adequate Stormwater Pollution Prevention Plan?
Protects Water Quality
Site Conditions
Schedule
Design
Notes: Must satisfy plan approval authority that all pollution sources will be controlled.
Incorporate the existing conditions, construction schedule, & finished design elements to protect water quality

## Slide 5
Managing Construction Site Runoff
is Not an Easy Task….
Budgets are tight, environmental protection
is often underestimated along with other
“unaccounted for” variables
The market is looking for a “one step solution”
answer and it does not exist
Enforcement is perceived as random and often
unevenly distributed regionally

## Slide 6
Requirements for all Projects
A permittee must select, install, implement, and maintain control measures (described in Part 4.0) at the construction site to minimize the discharge of pollutants as necessary to meet WQS’s (18 AAC 70).
Attainment of Water Quality Standards
CGP Part 3.1 Pg. 20

## Slide 7
Describe BMP’s to minimize erosion and sediment discharge.
Identify, reduce, or prevent the pollution of stormwater.
Prevent violations of water quality standards.
Identify, and assign maintenance responsibilities for BMP’s.
The Purpose of the SWPPP is to:

## Slide 8
The Key to a Successful SWPPP is…..
Assessment & Analysis
BMP Selection
Understanding & Implementation
Inspections & Documentation
Adaptive Management
Ketchikan
Site Specific:

## Slide 9
Straw Blanket
Wattle
Gravel Filter Berm
Silt Fence
Straw Mulch
What-Where-When?
Seeding
Soldotna
Notes: K-Beach Kenai

## Slide 10: Basics of a SWPPP
Narrative
Existing Site Conditions
Construction Schedule
Rainfall Data
Pollution Prevention Strategies & Responses
Drawings and Notes
Where & When BMPs Installed
BMP Performance Goals
Maintenance Procedures & Standards
Notes: Must satisfy plan approval authority that all pollution sources will be controlled.

## Slide 11
SWPPP Objectives:
• Stabilize the site as soon as possible
• Protect slopes and channels
• Reduce impervious surfaces
• Promote infiltration
• Control the perimeter of your site
• Protect receiving waters adjacent to your site
• Follow pollution prevention measures
• Minimize the area and duration of exposed soils
Notes: How do we describe this stage of construction in the SWPPP? Subdivision, Longview WA

## Slide 12
Identify the following qualified person(s) responsible for the following (Note: A small project may have all one person):
Storm Water Lead;
Updating the SWPPP according to Part 5.9;
Conducting inspections according to Part 6.0;
Conducting monitoring (if applicable) according to Part 7.0; and
Operating an Active Treatment System (if applicable) according to Part 4.6.7.
Storm Water Contact(s)
CGP Part 5.3.2 Pg. 36

## Slide 13
Contact Information
Responsible Parties
Permittee
At a minimum, the SWPPP must:
Identify the permittee for the site and any subcontractors that may work on the site, including the areas where the subcontractors are expected to conduct activities covered by this permit.
CGP Part 5.3.1 Pg. 36
Notes: The SWPPP should give the CESCL the information regarding chain of command. See SWPPP Guide, Chapter 2.B. and your construction general permit for the definition of operator.

## Slide 14
Exactly who is considered an operator is largely controlled by how the owner of the project chooses to structure the contracts with the contractors hired to design and/or build the project.
Subcontractors must be trained on appropriate BMPs and requirements in the SWPPP and should not disturb or remove BMPs. Some contractors will include specific penalties in subcontractor agreements to ensure subcontractors do not damage or remove BMPs.
The SWPPP must communicate
to everyone on the project!
CGP Part 5.3.2 Pg. 36

## Slide 15
Project Site-Specific Conditions
CGP Part 5.3.3 Pg. 37
Briefly describe the existing site-specific conditions, including:
Precipitation based on nearest weather station
Site Conditions – soils, topography, drainage, vegetation, etc.
Receiving waters

## Slide 16
The mean annual precipitation based on the nearest appropriate weather station;
CGP Part 5.3.3.1 Pg. 37
This is close but we can do better!

## Slide 18: xmacis.rcc-acis.org

## Slide 19
Site Conditions
Soils, Slopes, Vegetation, & Current Drainage Patterns
Describe the existing soil conditions including soil types, slopes and slope lengths, drainage patterns, and other topographic features that might affect erosion and sediment control.
Note any historic site contamination evident from existing site features and known past usage of the site.
Include this information on your site maps.
CGP Part 5.3.3.2 Pg. 37
Notes: Included on your site maps (See SWPPP Guide, Chapter 3.C.).
For more information, see SWPPP Guide, Chapter 3.A. for more information.

## Slide 20
Identify Receiving Waters,
Storm Drains &
Conveyances
Notes: Know where your water goes

## Slide 21
Receiving waters, such as impaired waters or waters listed in the Alaska Department of Fish & Game (ADF&G) Anadromous Waters Catalog.
CGP Part 5.3.3.3 Pg. 37

## Slide 22
www.adfg.alaska.gov/sf/SARR/AWC/index.cfm?adfg=maps.interactive

## Slide 23
Click your Project area.
Use the Zoom feature to find your Project.

## Slide 26
Identify Approaches to Protect Natural Resources
Protect Nearby Waters
Use a combination of techniques, including temporary fencing, signage, and educating staff and subcontractors.
Gravina Island

## Slide 27
In Water Work Conditions?
Environmental Commitments?
Windows for permitted work?
Timing Prohibition's?

## Slide 28
• Project type or function
• Sequence and timing of activities that will disturb soils at the site
• Size of the property including support activities and disturbance in acres
• General location map with construction site location and
any nearby waters or wetlands within 1 mile
• Other potential sources of pollution, asphalt, concrete, stucco, paint etc.
Nature of Construction Activity
CGP Part 5.3.4 Pg. 37

## Slide 29
Insert Video LID Part 1

## Slide 30
Will the discharge points
change during construction?

## Slide 31: Insert Video LID Phasing and Scheduling

## Slide 32
What is likely to be on site?
How might it pollute?
Identify Pollutants
& Pollution Sources
Be as specific as possible in your SWPPP about the BMPs you will use to address them.

## Slide 33
Incorporate sediment and erosion controls to protect permanent stormwater controls as they are constructed.
Notes: Such as wet ponds, swales, and bioretention cells. The construction site will drain into constructed storm systems. The planting strip behind the project is a stormwater treatment facility the hole to the left has outlets that drain into the Columbia river in the background.

## Slide 34
Site Map(s)
The SWPPP must contain a legible site map (or set of maps for large projects) showing the entire site and identifying the following site-specific information:
Hoonah
CGP Part 5.3.5 Pg. 37

## Slide 35
Use or create a topographic drawing that details:
North Arrow and bar scale;
Boundaries of the property where construction will occur;
Locations where earth-disturbing activities will occur, noting phasing;
Location of areas that will not be disturbed and features to be preserved;
Location of all storm water conveyances including ditches, pipes, and swales;
Locations of storm water inlets and outfalls, with a unique code for each;

## Slide 36
A permittee subject to the requirements of Parts 3.2 must include the location(s) of the storm water discharge sampling point(s). For a linear project, indicate which sampling points are considered substantially identical in accordance with Part 7.3.5*.
Monitoring Plan Only
Sampling Points
*Representative Discharge Point for a Linear Project.
CGP Part 5.3.5.18 Pg. 37
Notes: in accordance with Part 7.3.5;

## Slide 37
Locations of support activities.
Batch Plant
CGP Part 5.3.5.13 Pg. 37

## Slide 38: Locations of support activities
Storm water discharges from support activities (such as concrete or asphalt batch plants, equipment staging yards, material storage areas, excavated material disposal areas, borrow areas) (as defined in Appendix C), whether on-site, adjacent to, or offsite, provided the following:
The SWPPP must describe and identify the location of any storm water discharge associated with support activities.
CGP Part 5.3.5.13 Pg. 37
CGP Part 1.4.2.3 Pg. 10

## Slide 39
The support activity is directly related to the construction site required to have permit authorization for discharges of storm water associated with construction activity under this permit:
CGP Part 1.4.2.3.1 Pg. 10

## Slide 40: Locations of support activities
The support activity is not a commercial operation serving multiple unrelated construction projects by different permittees;
The support activity does not operate beyond the completion of the construction activity at the project it supports; and
CGP Part 1.4.2.3.2 Pg. 10
CGP Part 1.4.2.3.3 Pg. 10

## Slide 41
Appropriate control measures are identified in the Storm Water Pollution Prevention Plan (SWPPP) and pollutant discharges are minimized in compliance with Parts 3.0 and 4.0 of the permit.
CGP Part 1.4.2.3.4 Pg. 10

## Slide 42
Locations where authorized non-storm water will be used, including the types that will be used on-site.
Fort Yukon
CGP Part 5.3.5.14 Pg. 37

## Slide 43
Locations of all waters of the U.S. (including significant wetland areas > 10,000sf) on the site & located within 2,500 feet of the site boundary that may be affected by discharges from the site.
Your Next Job
CGP Part 5.3.5.15 Pg. 38
Notes: Sam can you identify this village?

## Slide 44
Projects near a Public Water System (PWS)
Where the project intersects a PWS drinking water protection area (DWPA) (see Part 5.3.5.16), notify the PWS contact.
Locations of existing PWS drinking water protection areas (DWPA) for PWS sources that intersect the boundary of the proposed project/permit area. The
site map must contain this information
Springs;
Wells; or
Surface water intakes.
CGP Part 5.3.5.16 Pg. 38
CGP Part 4.10 Pg. 34
Notes: The DEC has the Web Map Basic Instructions located on the CGP webpage.

## Slide 45
The DWPA can be found using the DEC interactive web map located at
http://dec.alaska.gov/das/GIS/apps

## Slide 46
Locations where storm water discharges to waters of the U.S. (wetlands, or an MS4)
CGP Part 5.3.5.17 Pg. 38

## Slide 47
Areas where final stabilization has been accomplished and no further permit requirements apply.
Goodnews
CGP Part 5.3.5.19 Pg. 38
Notes: Ask if the seeded areas have achieved final stabilization, how about the ditch with rock lining?

## Slide 48
Control Measures to Reduce Pollutant Discharges
The type of control, required maintenance & location.
The sequence during construction when it will be installed, operational, & any manufacturer’s specifications.
CGP Part 5.3.6 Pg. 38

## Slide 49
Sequencing
The general sequence of the stabilization practices that will be used to achieve temporary or final stabilization on exposed portions of the site as required in Part 4.5.
SWPPP must describe & document control measures
CGP Part 5.3.6.3 Pg. 38

## Slide 50
Treatment Chemicals
The type of treatment chemicals used on the site and a description of the general location of their use at the site, in accordance with Part 4.6.
SWPPP must describe & document control measures
CGP Part 5.3.6.4 Pg. 38

## Slide 51
The good housekeeping measures that will be used at the site, if any, in accordance with Part 4.8.
SWPPP must describe & document control measures
CGP Part 5.3.6.6 Pg. 38

## Slide 52
A description of spill prevention and response measures that will be used at the site, in accordance with Part 4.9. The permittee may reference the existence of other plans for Spill Prevention and Control and Countermeasure (SPCC) for the project, provided that a copy of the other plan(s) is kept with the SWPPP.
CGP Part 5.3.6.7 Pg. 38
SWPPP must describe & document control measures

## Slide 53
A description of all permanent storm water management controls that will be installed at the site, including their location, in accordance with Part 4.11.
SWPPP must describe & document control measures
CGP Part 5.3.6.8 Pg. 38

## Slide 54
Winter Shutdown
For projects that expect a winter shutdown, SWPPP must provide a description of the following:
Anticipated dates of freeze-up and spring thaw.
The methods to address winter considerations.
SWPPP must describe & document control measures
CGP Part 5.3.6.9 Pg. 38

## Slide 55
SWPPP must describe & document control measures
A description of maintenance procedures for control measures in accordance with Part 4.13.
Goodnews
CGP Part 5.3.6.10 Pg. 39

## Slide 56
Develop Site Maps
Include: Planned construction activities and stormwater practices for all stages of construction, protected areas, natural features, slopes, erodible soils, nearby waterbodies, permanent stormwater controls, etc.
Your SWPPP and site maps must reflect changes at your site.
Notes: Discuss the SWPPP change and how it goes against the Army corps permit requirement

## Slide 57
Use Site Maps to Track Progress
• Portable toilets
• Material storage areas
• Vehicle and equipment fueling and maintenance areas
• Concrete washouts
• Paint and stucco washouts
• Dumpsters or other trash and debris containers
• Spill kits
• Stockpiles
• Any other non-stormwater management BMPs
• Any temporarily removed structural BMPs
• Any changes to the structural BMPs
Notes: If a marked-up site map is too full to be easily read, you should date and fold it, put it in the SWPPP for documentation, and start a
new one. Construction sites are dynamic. As conditions change at the construction site, such as the locations of BMPs, your SWPPP must reflect
those changes.

## Slide 58
Update the site map as the site changes & BMP’s or facilities move

## Slide 59
A description of the training relevant to the construction activity and control measures used at the site.
SWPPP must describe & document:
CGP Part 5.3.6.11 Pg. 39

## Slide 60
Describe the type of construction and waste materials expected to be stored at the site with updates as appropriate and describe the measures for the handling and disposal of all wastes generated at the site.
Construction and Waste Materials
The SWPPP must:
clearing and demolition debris
waste soils removed from the site
construction and domestic waste
hazardous or toxic waste
sanitary waste
Kodiak
CGP Part 5.3.7 Pg. 39

## Slide 61
Tok
Locations of Other Industrial Storm Water Discharges
The SWPPP must describe and identify the location of any storm water discharge associated with support activities.
Including storm water discharges from dedicated asphalt and concrete plants that are covered by this permit.
CGP Part 5.3.8 Pg. 39

## Slide 62
The SWPPP must identify all authorized sources of non-storm water discharges.
The SWPPP must describe the good housekeeping measures used to control or reduce non-storm water discharges.
Non-Storm Water Discharges
Barrow
CGP Part 5.3.9 Pg. 39

## Slide 63
CERTIFICATION AND NOTIFICATION
The SWPPP must be signed and certified by the construction operator(s).
Attach a copy of the NOI and permit authorization letter.
“I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to assure that qualified personnel properly gathered and evaluated the information submitted. Based on my inquiry of the person or persons who manage the system, or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete. I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations.”
CGP Part 5.1.2.4 Pg. 36

## Slide 64: Personnel Qualifications in the SWPPP
Include in the SWPPP copies of the AK-CESCL cards or certificates for the Superintendent and SWPPP Manager, and for any acting Superintendent and acting SWPPP Managers. If the Superintendent or SWPPP Manager is replaced permanently or temporarily, by an acting Superintendent or acting SWPPP Manager; record in the SWPPP the names of the replacement personnel, the date of the replacement, and for temporary personnel their beginning and ending dates.
AK DOT Form 25D-127
Example DOT&PF requirement:

## Slide 65
Main Entrance Signage
Permit Authorization Number assigned NOI
Operator Contact Name
Operator Contact Phone Number
SWPPP Location or the name and phone number of the contact person
CGP Part 5.10 Pg. 42
Notes: Include all posting materials in the SWPPP. Have copies available to replace any damaged, even faded doccuments.

## Slide 66
Every site is different
Every SWPPP is unique
Practices will vary
Ketchikan

## Slide 67
SWPPP APPENDICES
A. Site Maps and Drawings
B. BMP Details
C. Project Schedule
D. Supporting Documentation:
    TMDLs
    Endangered Species
    Other Permits or Requirements
E. Delegation of Authority, Subcontractor Certifications
F. Permit Conditions:
    Copy of Signed Notice of Intent
    Confirmation of Delivery of NOI to ADEC
    Copy of Letter from ADEC Authorizing Coverage, with ADEC NOI Tracking Number
    Copy of Most Recent ADEC CGP
G. Grading and Stabilization Records
H. Monitoring Plan (If Applicable) and Reports
I. Training Records
J. Corrective Action Log
K. Inspection Records
* DOT SWPPP
Appendices vary

## Slide 68: When using the DEC SWPPP template:
 Control Measures:
Add a subsection to describe dedicated asphalt plants and/or dedicated concrete plants, give their locations and identify the BMPs that will be used to minimize pollutants from them. If there are no dedicated asphalt or concrete plants, then state that in the SWPPP.
Sea-Tac

## Slide 69: Proper BMP Specification, Application, Installation & Maintenance are Critical
The Right Thing
In The Right Place
At The Right Time
Notes: The right thing in the right place at the right time.

## Slide 71: What is a BMP?
Schedule of activities - Prohibitions of practices
Physical structures - Construction procedures
Other management practices to reduce pollution

## Slide 72: Design BMPs
Minimize disturbance (foot print) of project.
Maximize integration of existing land contours.
Minimize length and gradient of slopes.
Account for both onsite and offsite stormwater during construction.
Notes: Engage the class and encourage discussion.

## Slide 73: Procedural BMPs
Time major soil disturbance for dry season
Complete project in phases
Integrate erosion control and construction schedules (they don’t have to conflict)
Notes: Read slide.
Engage the class and encourage discussion.

## Slide 74: Physical BMPs
Implementation of erosion & sediment control practices in the field.
Must be a supplement to and not a replacement for design & procedural BMPs.
Notes: Read slide.
Section’s on SWPPP contains numerous BMPs that will be discussed in greater detail.

## Slide 75: General Principles
Retain duff layer, tundra, native topsoil & vegetation
Source control: preventing erosion is easier and cheaper than managing sediment
Divert run-on / runoff
Creativity is a BMP
Notes: Its important to control the water coming onto your project. Don’t let clean run-on water become dirty run off water from your project.

## Slide 76
BMP’s and your SWPPP should consider designs
to exceed your sites conditions.
Notes: Like anything, you can’t do it twice for less than doing it right the first time.

## Slide 77
Much Cheaper to start with
the right BMP first
BMP’s should meet & exceed designed performance
goals or outlast the strongest, longest storm
Notes: Plan ahead to avoid failures, use the information you have for risk management.

## Slide 78
Two Main Categories of BMPs in Stormwater & Erosion Control Manuals
Source Control BMPs
- Prevent the Problem
Runoff Conveyance & Treatment BMPs
  -Control Flows On & Around Your Site
  -Treat the Problem

## Slide 79
Minimize disturbed area and protect natural features and soil
Phase construction activity
Control stormwater flowing onto and through the project
Stabilize soils promptly
Protect slopes
Sediment Controls (the second line of defense)
Protect storm drain inlets
Establish perimeter controls
Retain sediment on-site and control dewatering practices
Establish stabilized construction exits
Inspect and maintain controls
Erosion Control (keeping the dirt in place) &
Minimizing the Impact of Construction

## Slide 80
Guidance Differs from Place to Place & Contracting Agency
Check With Your Local Agency & Owner
Notes: Details and instructions for BMP use etc. There are other manuals that have good details for BMP’s. When in another jurisdiction always use the local manual first then go outside for necessary BMP details and specifications. Note that the WA and OR BMPs may have regulatory elements that do not apply to Alaska.

## Slide 81: Alaska Storm Water Guidance
ADEC Storm Water Guide
  Program procedures
  http://www.dec.state.ak.us/water/wnpspc/stormwater/Guidance.html
DOT&PF Alaska Storm Water Pollution Prevention Guide
  Best Management Practices
  Department-Specific Requirements
  http://www.dot.state.ak.us/stwddes/desenviron/resources/stormwater.shtml
AK-CESCL
  Videos & training documents
  ak-cescl.com

## Slide 82: Most Used BMPs for Construction Sites Include:
Minimizing Soil Disturbance
Preserving Natural Vegetation
Good Housekeeping
Mulch/Seeding
Stockpile Covers
Silt Fence
Inlet Protection
Check Dams
Stabilized Rock Construction Entrances
Sediment Traps

## Slide 83: BMPs may Require an Engineer
Gradient Terraces
Interceptor Swales or Dikes
Orifice/Dams
Grass Lined Channel
Pipe Slope Drains
Subsurface Drains
Level Spreaders
Outlet Protection
Gravel Filter Berm
Sediment Traps & Ponds
Chemical Treatment
Filtration
Notes: Note picture. If this over flows where does it go? Could this be a hazard to the home directly downhill? Could infiltration of water in this area put down gradient structures at risk? Whose responsible for this if something happens?

## Slide 84: Stormwater Design Engineering Considerations
Identify Areas for Stormwater Infiltration
Identify Area for Stormwater Collection
Identify Construction Access
Identify Lay-Down Areas for Materials
Plan Contours to Eliminate Long and/or Steep Slopes
Notes: The picture is of a parking lot with stormwater infiltration and storage area. All asphalt drains into the center area. This is in north Idaho. There will be increased focus on “greener” design elements in all construction.

## Slide 85
Compost Sock
Coir Logs
Creek
Jute Netting
Coir Blanket
All Sites Require Multiple BMP’s
Seeding
Silt Fence
Gravel Access
in the right place, at the right time!
The trick is…
The right BMP,

## Slide 86
Rip Rap
Columbia River
Stockpile
BFM Spray Truck
USACE Bonneville Dam Fish Bypass
BMPs During Construction
Silt Fence

## Slide 87
Silt Fence
Slash Berm
Rock Berm
J Hook Sand Bags

## Slide 88
Stockpile Covered & Contained
Dump Truck on Gravel
Street Kept Clean
CGP Part 4.3.7 Pg. 26
Notes: Re cover pile when not working, Laborer with a broom & shovel.
The large export of this job made the stabilized entrance difficult to maintain. In retrospect it would have been cheaper to pave the access.

## Slide 89
Gravel Road
Wattles
Seeding
Stockpiles Covered
Tree Protection
The Right BMP in the Right Place at the Right Time Takes Planning

## Slide 90
Plan Implementation / Task Execution
Notes: Bypass creek to install outlet protection.
With any plan its only as good as it’s implementation and execution.
Now that we have a plan let’s do it!

## Slide 91
Creek Culvert Outlet
Energy Dissipation
Coconut Blanket
Hand Strewn Straw
Coconut & Straw Blanket
Straw Wattle
Notes: Work completed in one day including the creek bypass.

## Slide 92
What-Where-When?
Preserve
Vegetation
Silt Fence
Seeding
Wattles
RECP’s
Plastic
Channel
Lining
Notes: The next few slides show a good stabilization plan being executed on a project. The cut is being stabilized on the way down and the fill slopes are being stabilized on the way up.

## Slide 93
Finish as you go
Turn Liabilities into Assets
Manage Risk
Notes: Finish slopes are 1.5:1.
Slopes were stabilized as we proceeded. Subgrades were roughened. Straw wattles were countersunk and staked. 8” coarse compost blanket was applied throughout. Backsloping and vegetation retention continued as possible.
Note that permanent and temporary stabilization measures were integrated through design.
At this point in the excavation, the stormwater drainage shifted to the south.
We installed double silt fencing around sensitive area.

## Slide 94
Detail the planned process
Notes: The slope was stabilized as the fill was constructed.
We staked straw wattles, then spread coarse compost blanket, then hydromulched and seeded, before fill was completed.
PAM was applied on the fill slopes.

## Slide 95
Phase the Process
Notes: The lower slopes of the reinforced fill in the distance have been covered with coir matting, also before the fill is completed.
Note dedicated Baker tanks to manage runoff.

## Slide 96
Avoid preparing for spring runoff the hard way!
Plan Ahead

## Slide 97
A permittee must ensure that employees and subcontractors receive adequate training to ensure proper installation, maintenance, and removal of the control measures described in the SWPPP for the project.
Storm Water Lead & Training of Employees
CGP Part 4.14 Pg. 35

## Slide 98
Subcontractor Certification
Subcontractors must certify that they have read and will abide by the CGP & conditions of the project SWPPP.
DOT&PF specification 641-1.05 SIGNATURE CERTIFICATION REQUIREMENTS & DELEGATIONS.
*Subcontractors marching in line

## Slide 99
“Questions”