## Slide 1: CGP Requirements
Erosion Control Measures
January 2026
CGP Part 4.0 Pg. 22

## Slide 2: CGP Requirements
Goal of this section:
Become familiar with the types of erosion control measures that are required by the Alaska Construction General Permit (CGP):
  Delineate site
  Minimize amount of soil exposed
  Maintain natural buffer areas
  Control storm water discharges and flow rates
  Protect steep slopes
Learn about Best Management Practices (BMPs)
Learn the names and functions of common erosion control BMPs

## Slide 3: Delineation of Site
A permittee must generally delineate the location of:
All areas where soil disturbing activities will occur; and
Areas that will be left undisturbed.
CGP Part 4.2.1 Pg. 23
Notes: The smaller the clearing limits – the less erosion there will be
Vegetated buffer zones should be left in key locations to filter stormwater

## Slide 4
Courtesy Dwayne Stenlund CPESC MNDOT
USE A BARRIER THAT’S APPROPRIATE
FOR SITE SIZE AND CONSTRUCTION DURATION

## Slide 5
Delineation of Site
KEEP CONSTRUCTION ACTIVITY, EQUIPMENT,
& PERSONNEL OUT OF AREAS THAT DO NOT
NEED TO BE IMPACTED, OR CAN’T BE IMPACTED!

## Slide 6
Minimize the Amount of Soil Exposed during Construction Activity
CGP Part 4.2.2 Pg. 24
Notes: Always consider the resources on site, can they be salvaged and reused?

## Slide 7: Minimize the Amount of Soil Exposed during Construction Activity
Preserve Vegetation
Mulch
Fort Yukon
CGP Part 4.2.2 Pg. 24

## Slide 8: Delineating the Site Limits Helps Minimize Soil Erosion
The Smaller the Disturbance the Less Erosion Potential
By Clearing Less You Have Less to Restore, Maintain, and Monitor
Keep Vegetated Buffer Zones in Key Locations
Stay Out of Critical Areas
Notes: If you don’t mess it up you will not have to fix it.

## Slide 9
Tree Protection:
Protect the root zone
Preserves Vegetation
Limits Disturbance
Fairbanks
Notes: Note: Should the fencing be further out to fully protect the root zone? Thin soils and permafrost lead to larger root zones.

## Slide 10
Corrective Action?
Installed Correctly?

## Slide 11
Preserve native topsoil for later use with on-site stockpiles, unless infeasible; and
CGP Part 4.2.2.1 Pg. 24

## Slide 12
Sequence or phase construction activities to minimize the extent and duration of exposed soils.
Soldotna
CGP Part 4.2.2.2 Pg. 24

## Slide 13: Maintain Natural Buffer Areas
The buffer must be a minimum of twenty-five (25) feet wide, or the width as required by local ordinance.
Fairbanks
CGP Part 4.2.3 Pg. 24

## Slide 14
Buffer Zones
An undisturbed area or strip of vegetation
A living filter to reduce soil erosion and runoff velocities
BMP
WA C-102
DOT&PF – 20.00 Silt Fence
Notes: Leaving the natural soil and vegetation is a free BMP!

## Slide 15
Preserving Natural Vegetation
natural areas or as an individual clump
trees, shrubs and vines, grasses
Source Control BMPs
BMP
WA C-101
OR EP-2
Notes: The absolute cheapest BMP as it requires that you do nothing but leave it alone. Can be a resource to filter turbid water. Note the lower impact of the access road and clearing debris from the previous power-line construction.

## Slide 16
Clearing of vegetation that disturbs the vegetative mat and exposes soil is prohibited prior to obtaining authorization under this CGP permit.
Clearing Vegetation
CGP Part 4.2.4.1 Pg. 24

## Slide 17
Cutting of trees and brush while the ground is frozen without disturbing the vegetative mat early in the springtime to avoid adversely affecting migratory birds or their nests is allowed prior to the NOI.
If clearing disturbs the vegetative mat and occurs after the onset of spring thaw or above freezing temperatures cause melting of snow, the permittee must develop a SWPPP and submit an NOI. Operators must receive authorization and comply with the terms of this permit prior to such clearing.
Tununak
CGP Part 4.2.4.2 Pg. 24

## Slide 18
Control Stormwater Discharges & Flow Rates
Goodnews
CGP Part 4.2.5 Pg. 24

## Slide 19: Control Stormwater Discharges & Flow Rates
Mostly a designer issue except when:
Contractor modifies designed facilities
Contractor adds temporary facilities not shown on plans
Contractor pumps water off site
Ketchikan
CGP Part 4.2.5 Pg. 24
Notes: Probably the biggest challenge for construction site operators.

## Slide 20: Clean Water Diversions
Photo Courtesy DNREC
Notes: Bypass clean flows around your project

## Slide 21
Culvert Replacement
Notes: Is this type of culvert replacement and diversion permitted in Alaska?
Fish and wildlife, FHA Permit, does not permit working in flowing water.

## Slide 22
Culvert with Streambed
Material placement
Notes: These are the same guys attempting to remove themselves from the gene pool

## Slide 23
Eagle River Loop Road Temporary Bypass
Work Area
Sump Discharge
Diversion Sump Berm
Bypass Diversion Berm
Bypass Flow
Eagle River
Notes: Dewatering and bypass are different, The pumps here are really part of the bypass

## Slide 24
Culvert
Extension
& Headwall
Notes: Pumps from the excavation would be dewatering

## Slide 25
Juneau
Notes: The left side is good examples. The right pictures are taken from the same location the culvert discharge was built to bypass the flow around the workarea and the outlet needs stabilization. The lower right is the existing channel and can be left as is.

## Slide 26
Any Diversion Ideas?
Ketchikan
Notes: Solicit diversion ideas from the class.

## Slide 27
Temporary Energy Dissipation

## Slide 28
Run On Flow
Placed By Project
Native Soils
Divert stormwater around the site so that it does not flow
onto the project site & cause erosion of exposed soils.
CGP Part 4.2.5.1 Pg. 24

## Slide 29
Slow down or contain storm water that may collect and concentrate within a site and cause erosion of exposed soils.
CGP Part 4.2.5.2 Pg. 24

## Slide 30
Place velocity dissipation devices (e.g., check dams, sediment traps, or riprap) along the length of any conveyance channel (of erodible materials) to provide a non-erosive flow velocity.
CGP Part 4.2.5.4 Pg. 24
Notes: Dozers do not make good check dams.

## Slide 31
Place velocity dissipation devices where discharges from the conveyance channel or structure join a water course to prevent erosion and to protect the channel embankment, outlet, adjacent stream bank slopes, and downstream waters.
CGP Part 4.2.5.4 Pg. 24

## Slide 32
Install permanent storm water management controls, where practical, so that they are functional prior to construction of site improvements.
CGP Part 4.2.5.5 Pg. 24

## Slide 33
Permanent storm water retention or detention facilities must be constructed as one of the first steps in grading. Detention facilities must be functional prior to construction of site improvements (e.g., impervious surfaces).
Fairbanks

## Slide 34: Armor Areas of Concentrated Flow & Discharge
Glenn HWY
Notes: Use riprap rock to stabilize outlets. What happened with the rock placement.

## Slide 35
Track Walked Topsoil with Organics
RECP
Stabilized Conveyance
Stabilized Outlet

## Slide 36
Picture Courtesy DNREC
Slow down or contain storm water that may collect and concentrate within a site and cause erosion of exposed soils

## Slide 37
Prevents scour at conveyance outlets
Minimizes the potential for downstream erosion
BMP
WA C-209
OR RC-2
Outlet Protection

## Slide 38
Temporary Pump Discharge Energy Dissipater
Juneau
Notes: The hole was formed by using any energy dissiaption before the tarp and plastic was used.

## Slide 40
What do we do next?
Glen Hwy

## Slide 42
Soldotna
Limit disturbance
Stabilize early

## Slide 43
Soldotna
Be prepared
For the next season!

## Slide 45
Notes: Curb Appeal. Bales the wrong way, not enough stakes, Multiple Blowouts.
Does this demonstrate compliance or insanity?

## Slide 46
Erosion Control Technology
In Action
Shopping Cart Check Dams
“URBAN GABIONS”

## Slide 47: Channels Have Design Guidelines & Local Requirements
Temporary conveyance channels must be designed, constructed, and stabilized to handle flows from designed frequency storm events of the developed condition.
Stabilize outlets of all conveyance systems to prevent erosion. (Scour, Streambank)
Typical Design storm is 2yr – 24hr

## Slide 48
Grass-Lined Channels
Channel Lining
Protect channels from erosion
Less than 10% slope
Select liner adequate for shear stress
BMP
WA C-201 OR RC-5
BMP
WA C-202 AK DOT&PF 18.00
Emmonak

## Slide 49: RECP = Rolled Erosion Control Product
Reduces Rainfall Impact
Helps Establish Vegetation
Protects Planted Soils From Erosion
Enhances Filtration
Traps Sediments
Retains Soils for Root Growth

## Slide 50: Types of RECPs
Erosion Control Blankets
Mulch Netting
Open Weave Textile
Turf Reinforcement Mats - TRMs

## Slide 51: Add RECP Part 1 Video

## Slide 53
ECTC
Categories
Cross Referenced
With Product

## Slide 54: RECPs in Channels
Grade, Smooth and Compact Channel
Seed & Amend Soils Properly
Dig 6x6” Trench at Beginning of Flow
Rollout RECP in Direction of Flow
Emmonak
ECTC RECP Video

## Slide 55: Important Keys for RECPs in Channels
Start in Center & Work Up Channel Sides in Larger Channels
Minimize Seams & Avoid Seams in Area of Concentrated Flows in Larger Channels
The Higher the Expected Flow the More Staples Will be Required
TRMs Should Be Used When Water Velocity & Sheer Stress is High

## Slide 56: RECPs in Arid Climate Channels
Synthetic RECPs Work Better in Dry Conditions
Vegetation is Sparse & Grows Slow
They Last Longer
Barrow

## Slide 57: Check Dams
Notes: Note haw many become necessary, would lining be a cost effective alternative?

## Slide 58: Check Dam Design
Check Dams Should Be Low in Middle to Allow Water Spillover
Do Not Let Water Flow Around Sides
Sediment Should Collect Behind Dams
Bottom of Check Dam Should Be Equal Height with Top of Next Dam

## Slide 59
Beware of
The End Run
Check Dam
Glenn Hwy at Hicks Creek

## Slide 60
Phase 1
Notes: Good Effort, but what might be lacking in design or installation?

## Slide 61
Phase 2
Notes: This is not good.
This costs me money.

## Slide 62
Phase 3

## Slide 63
Sea-Tac
Notes: Ask for comments, What BMP’s are here, are they installed correctly? Do they need corrective actions? TRM with check dams but the check dams are not the correct shape.

## Slide 64
Check Dam Shape & Spacing
TRM Channel Lining
Where will the water go?
Sea-Tac

## Slide 65
Critical Thinking
Exercise
Old Glenn
Notes: What would you do different the next time? How effective are these efforts in reducing erosion?

## Slide 67
Reduce the velocity of runoff
Elevation of toe equal to discharge
Check Dams
BMP
WA C-207
OR RC-11
AK DOT&PF 31.00-33.00
Notes: Toe to Top elevation, staircase, when do you go to channel lining?

## Slide 68
What's wrong here?

## Slide 69
What are we trying to do here?

## Slide 70
Velocity Control
Reduces flow velocity
Dissipates energy
Retains sediment
Check Dams
BMP WA C-207
OR RC-11
AKDOT&PF 31.00-33.00
Dalton HWY

## Slide 71
Dalton Highway

## Slide 72
Retains Sediment
Slows Velocity
BMP
WA C-232
DOT&PF – 16.00 Rock Filter Berm
Gravel Filter Berm

## Slide 73
Frozen Silt Wrapped in Geotextile
Stabilized Site
Kotzebue

## Slide 74
Convey stormwater away from or over bare soil
Need Energy Dissipation
BMP
WA C-204
OR RC-1
DOT&PF -22.00
Pipe Slope Drains
Soldotna, AK
Notes: 74
Take water to the bottom of the hill. Energy dissipation at the outlet.

## Slide 75
Soldotna, AK
Filter Sock
Pipe Slope Drain
Temporary Liner

## Slide 76
Alaska BMP’s
Silt Fence
Brush Barrier
Vegetative Buffer
Seed & Mulch
Wattle
Plastic Sheet Slope Drain
Soldotna, AK

## Slide 77
Pipe Slope Drains & Sediment Traps

## Slide 78
Always plan for moving water
Slow the flow
Armor against the flow

## Slide 79
Eagle River
Raindrop
Protection
Conveyance
Perimeter Control
Four Wheeler
Deterrence
Protect Steep Slopes
CGP Part 4.2.6 Pg. 25

## Slide 80
Design and construct slopes in a manner that will minimize erosion
CGP Part 4.2.6 Pg. 25

## Slide 81
Reduce slope length with terracing and diversions
Reduce slope steepness

## Slide 82
Roughening slope surfaces
Track walking
Imprinting
Stamping
Raking

## Slide 83
Interceptor dikes
Swales
Pipe slope drains
check dams
Divert concentrated flows of storm water away from and around the disturbed portions of the slope.
CGP Part 4.2.6.2 Pg. 25

## Slide 84
Stabilize exposed areas of the slope in accordance with Part 4.5.
Kodiak
CGP Part 4.2.6.3 Pg. 25

## Slide 85: Protecting Slopes
Slopes are Prone to Rilling & the Formation of Gullies
Slope Steepness Should Be Lessened Where Possible
Slope Length Should Be Decreased Wherever Possible
Many BMPs Which Protect Slopes Must Be Engineered
Takotna

## Slide 86
Anchorage
Urban Pad Slope Protection

## Slide 87
Protecting Slopes is Difficult
Notes: Slopes were complete and seeded.
Know the limits of the seed, germination, soil health & chemistry.

## Slide 88: Insert Video Seed Preparation/Track Walking

## Slide 89
Notes: This is only preventing further damage.
The slope still needs to be rebuilt and stabilized.

## Slide 90
Notes: A very expensive change in design.

## Slide 91
Seed, Silt & Fertilizer Creep
Kongiganak
Notes: The silt and seed is being displaced and washed down the slope

## Slide 92
Some Seed, Some Track Walking, Some Jute Net
Maybe we’ll get lucky and grass will grow…
“Luck is the residue of design”
-John Milton
Kongiganak

## Slide 93
Slope Aspect & Orientation
Notes: Think of northerly & southerly facing slopes

## Slide 94
Track Walking
Hicks Creek
Roughen Slopes to Reduce Erosion Potential up to 55%

## Slide 95
What’s happening here?
Notes: Correct track-walking on slope. In Correct track-walking in foreground

## Slide 96
Track Walking Increases Soil Texture,
Also Increases Surface Area
BMP Surface
Roughing
WA C-130
OR EP-3
DOT&PF 30.00
BMP Bonded Fiber Matrix Mulch
Notes: How much extra product should be budgeted for the increased surface area?

## Slide 97
Straw Double Net Blankets
Visible Straw Creep
BMP – Nets & Blankets
The Right Product For
Specific Site Conditions
Notes: Straw Creep, Limatations of materials relative to slope length and steepness.

## Slide 98: Composition of RECPs
Straw
Coconut / Coir
Excelsior
Polypropylene
Nylon
Jute
ANC
Functional Longevity
Tensile Strength

## Slide 99
Straw
Coconut
Straw Coconut
3 yr
2 yr
1 yr
Functional Longevity

## Slide 100
Notes: Various blanket applications.
Note various planting repair strategies.

## Slide 101: RECP Installation for Slopes
Surface Must Be Smooth & Compacted
Match Proper Seed to Site Conditions
Dig 6x6” Trench 3’ Back From Slope Crest
Place, Staple, Backfill & Compact RECP into Trench
Unroll RECP Downslope by Hand For Soil Contact
Secure RECP With Staples 3’ Vertically & 18-24” Horizontally or Manufacturers Instructions
Shingle Overlap
Toe Anchor RECP 2’ Below Toe of Slope
Notes: RECP Video After This Slide

## Slide 102: Add RECP Part 2 Video

## Slide 103
Proper Installation is Critical
Notes: Excelsior blanket blown off slope

## Slide 104
Will your choices come back to haunt you?
Photo Courtesy Stoney Wright
Notes: Plastic netting is not degrading and has become a hazard on its own.

## Slide 105
Cut Slope Stabilization
Finish as you go!
Ketchikan
Notes: The sludge has covered a 12 inch coir log.

## Slide 106
Blanket Anchored With Sandbags
Frozen Ground?
Wattles Anchored
With Form Stakes
Anchorage
Notes: Frozen ground prevented the installation of staples so sand bags were used. Concrete form stakes used for the wattle install.

## Slide 107
Turf Reinforcement Mat
Hydraulic Seeding & Mulching Infill

## Slide 108
Blanket
Cellular
Confinement
Geotextile
Soil Infill
When it Absolutely, Positively, has to Hold Tight
Notes: All BMP’s have design levels of performance.
There seems to be no limit to technology.

## Slide 109
Wasilla
Cellular Confinement

## Slide 111: Insert Video Fiber Rolls for Erosion Control

## Slide 112
Hydroseed Slopes with Wood Fiber Mulch
Straw Wattles Reduce Slope Length
Nancy Lake

## Slide 113
Wattles

## Slide 114: Straw Wattles Installed on Contour Across Slopes & Perimeter
Notes: Consider trip hazards and safety with stakes.

## Slide 115
Frozen Ground Solutions
Rebar Stakes & Wire
Fox Spring
Notes: Using the re-bar and wire to secure wattles in the frozen ground. Will the stakes require removal? Are they a hazard?

## Slide 116
Reduce water velocity
Spread the flow of rill and sheet runoff
Capture and retain sediment
Placed in shallow trenches and staked on contour
BMP
WA C-235
OR SC-7
DOT&PF – 10.01
Glenn Hwy
Straw Wattles
Notes: Wattles break up slope length and reduce erosion. Note wattle installed over the culvert as a perimeter control.

## Slide 117
Standard on contour installation
Drier climate

## Slide 118
Sloped installation
Wetter climate

## Slide 119
Notes: Step by step implementation

## Slide 120
J Hook or Smile
Sediment Deposition Area
Using Wattles to Direct Flows
Straw Coconut RECP

## Slide 121
Direct flows off slopes

## Slide 122
Required Control Measures
Soil Stabilization
Minimum Requirements for Soil Stabilization
Temporary Stabilization
Final Stabilization
Stabilization Requirements for Terminating Permit Coverage
CGP Part 4.5 Pg. 27

## Slide 123
Applicable stabilization control measures include:
• Temporary and permanent seeding;
• Sodding;
• Mulching;
• Rolled erosion control product;
• Compost blanket;
• Soil application of Polyacrylamide (PAM);
• Early application of gravel base on areas to be paved; and
• Dust control.
CGP Part 4.5 Pg. 27

## Slide 124: Stabilize Soils
Stabilization efforts
will affect water quality
Parks Hwy
Notes: Exposed bare soils is the source of soil erosion – they must be protected

## Slide 125
Phasing/Sequencing
Minimum Requirements for Soil Stabilization
A permittee must consider the selection and implementation of control measures and the sequence of project construction as they apply to the project site.
Anchorage
CGP Part 4.5.1 Pg. 28
Notes: In areas where dust control is an issue, your SWPPP should include BMPs for wind-erosion control. These consist of mulching, wet suppression (watering), and other practices

## Slide 126
Erosion Control & Stabilization:
Deadline to Initiate Stabilization
Stabilization of disturbed areas must be initiated immediately whenever any clearing, grading, excavating, or other soil disturbing activities have permanently ceased on any portion of the site or temporarily ceased on any portion of the site and will not resume for a period exceeding:
Anchorage
CGP Part 4.5.1 Pg. 28

## Slide 127
Initiate Stabilization
Initiated Immediately….
Where mean annual precipitation is :
>40 inches within 7 days
<40 inches within 14 days
CGP Part 4.5.1 Pg. 28

## Slide 129
Deadline to Complete Temporary Stabilization Activities
The following are required to be completed as soon as practicable, but no later than 14 calendar days after initiation of soil stabilization measures for:
Vegetative stabilization, all activities necessary to initially seed or plant the area to be stabilized; and/or
Non-vegetative stabilization, the installation or application of all such non-vegetative measures to meet the definition of temporary stabilization.
Parks Highway Broad Pass
CGP Part 4.5.1.2 Pg. 29

## Slide 130
The permittee must within 7 calendar days of initiating final stabilization complete or continue maintenance for the following on any portion of the site that has reached final grading and for areas where clearing, grading, excavating, or other earth disturbing activities have permanently ceased:
All soil conditioning, seeding, watering, mulching, and any other required activities for the establishment of vegetative cover;
The installation or application of all such measures for vegetative cover; and/or
The placement of non-vegetative final stabilization measures.
Deadline to Complete Final Stabilization
CGP Part 4.5.1 .5 Pg. 30

## Slide 131
Anchorage

## Slide 134
Stabilization Requirements for Terminating Permit Authorization
To terminate authorization under this permit, final stabilization must be achieved on all portions of the site for which a permittee is responsible and all ground disturbing construction activity or use of related support activities must be completed.
CGP Part 4.5.2 Pg. 30

## Slide 135
Winter Shutdown
The permittee must identify the anticipated dates of fall freeze-up & spring thaw
Plan for winter shutdown and properly install BMPs.
Frozen ground is not considered stabilization.
Cook Inlet
CGP Part 4.12.1 Pg. 34

## Slide 136
A permittee must ensure the following measures are complete prior to fall freeze-up:
  Temporary or final stabilization for conveyance channels,
  Temporary or final stabilization for disturbed slopes, soils, and stockpiles
Proper installation of control measures in anticipation of spring thaw.
Where temporary stabilization is precluded by snow cover or frozen ground conditions, prior to the anticipated date Fall Freeze-up, stabilization measures must be initiated as soon as practicable following the actual spring thaw.
CGP Part 4.12.1.1 Pg. 34

## Slide 137
Insert Video 1 coming out of winter shutdown

## Slide 138
Insert Video Going into winter shutdown

## Slide 139: Stabilize Soils With Hay/Straw Mulch
Hay/Straw Mulch Erosion Reduction
½ Ton Per Acre | 75%
1 Ton Per Acre | 87%
4.5 Tons Per Acre | 98%

## Slide 140
Provide immediate temporary protection from erosion
Enhances plant establishment
Common mulches:
  Straw
  Wood chips
  Compost
  Bonded fiber matrix
BMP
WA C-12O
OR EP-8
AK - 9
Mulching

## Slide 141: Vegetation & Erosion Prevention
Grass Seeding/Sod Erosion Reduction
40% Cover | 90%
60% Cover | 96%
90%+ Cover | 99%

## Slide 142
On disturbed areas that have reached final grade or that will remain unworked for more than 30 days.
Schedule stabilization around seeding windows.
Protect seed with mulch or plastic in cold weather.
Irrigate in dry weather until 75% cover established.
BMP
WA C-120
OR EP-5 , EP-6
AK - 10
Temporary &
Permanent Seeding
Notes: Temporary seeding must be employed during prolonged exposure durations.

## Slide 143
Seed Bed Preparation
Seeding Methods

## Slide 144: Standard Operating Procedure
Seeding was a normal operation conducted as needed throughout the active construction period.
Tuntutuliak

## Slide 145
Tuntutuliak

## Slide 146
Tuntutuliak

## Slide 147
Aerial Seeding

## Slide 148
Insert Video Salvaging Topsoil

## Slide 149: Preserve Topsoil
Unless infeasible, preserve areas of native topsoil onsite (CGP)
  Helps provide a growing medium for vegetative stabilization measures
  Better vegetative stabilization reduces erosion rates and increases infiltrative capacity.

## Slide 150: State Seed Regulations
All seed sold in the state must be clearly labeled or tagged with the following information:
Common name of seed
Where it was grown
% pure seed
% weed seed
% inert matter
% other crop seeds
% name and number/lb of each restricted weed seed
% germination w/ month and year of test
% hard seed
Fox

## Slide 151
Insert Video Factors that affect vegetation establishment

## Slide 152: State Seed Regulations cont.
Name and address of seed distributor
Lot number or other lot identification
Mixed seed will state the blend

## Slide 153
Show name and variety of each kind by percent in order of predominance w/ lot numbers
% weed seed, % inert matter
Name and amount of restricted weeds
Germination test information and dates

## Slide 154: Why use native seed?
It prevents the introduction of potentially unwanted pest species.
They are truly adapted to the area.
Their appearance is more pleasing.
It is a local business
Last but not least, it is required under Federal Rules

## Slide 155
Dormant Seeding
Remains un-germinated until next growing season
Not immediately effective
Seed after first hard killing frost
Not on crusted or more than 4 inches of snow
Include annual and perennial species
Seed needs to be kept in place
Notes: Seeds can be displaced by break up or washed away by snowmelt. Dormant seeding becomes more risky as slope steepness increases. Using blankets or mats over seeds will keep them in place over winter and during breakup. If seeds germinate and then frost hits many plants will die.

## Slide 156
Have vegetation ready for
Breakup & Spring Feeding
Nome

## Slide 157
Hydromulching
Photo Courtesy Stoney Wright CPESC

## Slide 158
Insert Video Hydro Mulch

## Slide 159
BMP
WA C-
OR EP-8
AK - 9
Notes: Tracking is good, Seeding is not. Cover the entire slope, one weak link in the chain…..

## Slide 160
View from the bottom up
Notes: Note how the coverage looks better when viewed from the direction of the spray.

## Slide 161
View from the top down
Notes: The spray was applied from the bottom of the slope, note all the surface area that was not covered when viewed from the top. Same slope in the exact same place.

## Slide 162
Insert Video Hydraulic Mulch

## Slide 163
Nets and Blankets
Prevent erosion & hold seed and mulch in place
Reinforce turf
Organic: biodegrade in place, 1-5 years
Inorganic: long term high stress applications
Source Control BMPs
BMP
WA C-122
OR EP-10
AK - 14
Notes: Difference between nets and blankets.

## Slide 164
Provide a suitable growth medium for final site stabilization
What does your contract stipulate you provide
Top soiling
BMP
WA C-125
OR EP-4
Notes: When vegetation is your finished product provide a quality soil for good growth.
NOT = Final Payment

## Slide 165
Soil Amendments:
What have we tried?
What are we trying?
Kodiak
Compost

## Slide 166
Insert Video Biotic Soil Amendment/Media

## Slide 167: Composting Stabilization
Improves Soil Structure
Absorbs More Moisture
Provides Soil Nutrients
Suppresses Diseases
Degrades Compounds/Pollutants
Increases Surface Porosity
Mimics Nature
Facilitates Growth
Notes: Compost Blanket = $30 per sq. yard

## Slide 168
Is importing topsoil really needed for establishing vegetation?
The Biotic Approach Asks…
Notes: If our old revegetation technique isn’t working for us we have to ask: is there another way of looking at this problem?

## Slide 169
Poor Soils
Low Organics
Low Fertility
Topsoil alternative
Dillingham

## Slide 170
Surface Prep
Biotic Soil Amendments
Dillingham

## Slide 171
Biotic Soil Amendments
Dillingham

## Slide 172
Use existing equipment,
Simpler mobilization,
$$$ Saved $$$

## Slide 173
Kenai Riverbank Stabilization
Biotic Soil Amendments in action

## Slide 174
Shoreline armor

## Slide 175
Shoreline armor

## Slide 177: Tackifiers & Binders
Tackifiers are uses as a tie-down for:
  Soil;
  Compost;
  Seed; or
  Mulch.
    Four types: Hydraulic Mulch, Hydraulic Matrix, Bonded Fiber Matrix, Mechanically Bonded Fiber Matrix

## Slide 178
Extreme Topography Complicates Stabilizing Soils
and:
Records of Disturbance & Stabilization
-or- Grading Logs

## Slide 179
Steep Slope Blanket Installation
Safety First