## Slide 1
8. SWPPP Control Measures:
Sediment Controls
Minimum measures
Inspecting for compliance
Recognizing deficiencies
January 2022

## Slide 2
Behold: The worlds most effective silt fence
Nome
Sediment Controls
Notes: What exactly is this silt fence doing, comment on the repeated misuse of silt fence in the construction industry. Open the discussion about how sediment controls are trying to prevent sediment from getting into surface waters, the sediment controls should not be in the waters.

## Slide 3: Storm Drain Inlet Protection Measures
A permittee must install appropriate protection measures to minimize the discharge of sediment prior to entry into the inlet
2021 CGP 4.3.1
Notes: Do not spend a lot of time working on drain inlets without protecting it properly

## Slide 4
ANC
Will traffic impact your BMP?
Will your BMP divert flow somewhere else?
Is there a detail for this that assists an inspector?
Notes: Many times inlet protection can get in the way of traffic or be destroyed by traffic. An inspector must pay attention to inlet protection that diverts flows somewhere else like this one as the increased flows to other areas may cause problems. The diversion would be created because the BMP will bypass the flow around the inlet to the next one down gradient.

## Slide 5
Protect culverts from sediment deposition
Anchorage

## Slide 6
Water Body Protection Measures
2021 CGP 4.3.2
No perimeter protection measures in place
-Some mulch, should be thicker
Notes: There is no BMP between the construction site and the receiving waters.

## Slide 7
Water Body Protection Measures
A permittee must install appropriate protection measures to minimize the discharge of sediment prior to entry into the water body for water bodies located on site or immediately downstream of the site.
Tok
2021 CGP 4.3.2
Notes: Outlet protection is in and the wattle is the waterbody protection measure mulch and seed on the soils.

## Slide 8
Shoreline Protection?
Notes: This is only for a little humor, if an instructor has no humor or desire to inject any levity to the class delete it or ignore it.

## Slide 9
Sitka
Aggregate Gradation for Stabilization
Notes: Interlocking gravel is great stabilization. Depending on the forces it will be exposed to you need to use larger rock. This is true for all shear stress lining, ditches, overflows, outlets etc.

## Slide 10
How Should We do Perimeter Control Here?
Glacier Highway
Notes: Using the finished rock material to create a sediment control berm as the slope is constructed.

## Slide 11
Glacier Highway
Notes: Note the height of the berm will detain sediment washed off the roadway

## Slide 12
Perimeter Controls On the Cheap and Easy
Glacier Highway
Notes: Note the big rock is the same in the previous slide to show scale and height

## Slide 13
Gravel Berm Perimeter Control
Glacier HWY Juneau
Notes: This is a gravel filter berm that will be the perimeter control and simply become part of the fill.

## Slide 14
Glacier HWY Juneau
Notes: With the fill complete the gravel filter berm is simply part of the fill.

## Slide 15
Introducing:
The All NEW!
BERMANATOR
Notes: This is a unique invention from the field. Nicknamed the bermanator.

## Slide 16
Notes: A conveyer to build the berm with an excavator.

## Slide 17
Glacier HWY Juneau
Notes: The perimeter controls do not go through the receiving waters but should go around them.

## Slide 18
Glacier HWY Juneau
Use riprap that is 4” or greater
Install fabric to prevent soil erosion beneath the riprap
Stabilize all disturbed areas immediately after work is complete
Inspect the outlet after a heavy rain event

## Slide 19
Describe the sequence and timing of activities that disturb soils and of BMP implementation and removal. Phase earth disturbing activities to minimize un-stabilized areas, and to achieve temporary or final stabilization quickly.
Prior to embankment fill:
1- Install Perimeter berm at OHW
2- Place 4 “ gravel filter layer on berm
Upon completion of the approach fill:
1- Place geotextile fabric
2- Place rip rap on slopes
See detail Plan sheet xxxxx
Notes: An example of using the same idea for a water crossing perimeter control and embankment stabilization. Bern height may vary depending on size of embankment fill

## Slide 20: Example DOT&PF BMP
Existing Grade
Berm 4’’- 8’’ Varies
Washed
Pea Gravel
OHW
Fill
area
No published BMP manual was used for this design.
Designed by Danny Dirt PE, AK-CESCL #007
8oz Geotextile filter fabric
Riprap

## Slide 21
Perimeter Control
Notes: Bridge decks and temporary crossings always present challenges to perimeter sediment controls.

## Slide 22
Gravel Filter Berm &
Embankment Stabilization
Notes: Here a gravel filter berm is also acting as final stabilization.

## Slide 23
Notes: When the girders are set the stabilization is complete.

## Slide 24
Different Risks = Different Stabilization Measures
Fairbanks
Notes: The different slopes, proximity to the water, schedules for the next phase should drive the decisions about the rock size to stabilize the areas.

## Slide 25
In Water Controls
2021 CGP 4.3.3
Lake Hood
Notes: Provide a place for the eroded material to collect on your property.
Remove sediment from the stormwater.

## Slide 26
Pity the BMP’s on the edge of the earth
Site Discharge
Receiving Water
Barrow
BMP?
Notes: Make a little fun of silt fence, then introduce alternative method with the wattle

## Slide 27
Was it inspected?
Do we know how to inspect?
Anchorage
Notes: Improper installation when found in the field begs two questions, are we inspecting? Are we qualified to do inspections?

## Slide 28
Gustavus
28
Notes: Note sediment deposition past the silt fence, what is the purpose of the silt fence. Where should the fence be?

## Slide 29
Specialty Perimeter Sediment Controls
Temporary Crossings
Bridge Decks

## Slide 30
Perimeter Control?
Notes: This is bridge crossing and the silt fence is simply a flap on the asphalt and some sand bags to try to hold it down. Construction traffic is breaking the bags and the effectiveness was never really there. This situation comes up a lot, if the sediment control is not tightly sealed to the surface flow will simply go under it. In this case right into the creek.

## Slide 31
Notes: Directing flow off a bridge crossing situation to the surrounding area is usually the preferred method for dealing with these perimeter control situations.

## Slide 32
Simple Solutions
8oz Drainage Filter Fabric
Weep Holes (Maybe)
2x6 lumber or larger
Adhesive / Sealant
Notes: This is only one idea for dealing with this situation. No matter what a project chooses to use it must be in contact with the asphalt to prevent water from getting under the installation.

## Slide 33
Bridge Deck Perimeter Control
Ketchikan
Notes: These are different examples of bridge deck perimeter controls, note the steel plate preventing the wear on the geotextile.

## Slide 34: Stabilized Construction Vehicle Access & Exit Points
A permittee must establish construction vehicle access and exit points and they must be stabilized.
Anchorage
Rattle
Racks
2021 CGP 4.3.4
Notes: Trackout is extremely dirty when rain washes it off – Regulators will be looking at this very frequently – perhaps the most public construction erosion control problem there is.

## Slide 35
Stabilized Construction Vehicle Access & Exit Points
35

## Slide 36
Juneau
2021 CGP 4.3.5
Notes: This means more than just cleaning up the track out. “Prevent” is the key word.

## Slide 37
Automated Wheel Wash
Notes: Street sweeping can be very expensive on projects that involve a lot of export. If traffic must enter the site and drive through dirt and mud there will be trackout, a wheel wash may be necessary to prevent the trackout. Most commercial washes usually need extra capacity in the reservoir and a flocculent to get desired results.

## Slide 38
Is tracking out onto a dirt road really track-out?
If sediment escapes the construction site, off site accumulations of sediment must be removed at a frequency sufficient to minimize off-site impacts.
2021 CGP 4.3.4
Kongiganak
Stabilized Construction Vehicle Access and Exit Points
Notes: Note the heavy equipment at the project, this is a haul road from the barge landing being used for the aggregate import. Does the trackout need to be cleaned up to “minimize” off-site impacts? If washed into the roadside ditch where will it go? Does the ditch discharge into a water of the US?

## Slide 39
Sediment Basins
4.3.9.1 For common drainage locations that serve an area with 10 or more acres disturbed at one time, a temporary (or permanent) sediment basin that provides storage for a calculated volume of runoff from the drainage area from a 2-year, 24-hour storm, or equivalent sediment control measures, must be installed, maintained, and used where practicable until final stabilization of the site. 10 acres of contributing drainage requires a sediment basin
4.3.9.1.1 Where no such calculation has been performed, a temporary (or permanent) sediment basin providing 3,600 cubic feet of storage per acre drained, or equivalent sediment control measures, must be installed and used where practicable until final stabilization of the site.
Wasilla
2021 CGP 4.3.9
Notes: 10 acres of disturbed area at a time contributing to a single discharge point.

## Slide 40
Note: No installation of sediment basins should be installed in permafrost areas.
2021 CGP 4.3.9.4

## Slide 41: Control Dewatering
Plan the dewatering activity
  Have an approved method
  File NOI for DEC permit if necessary
  Involve the approval agency
  Monitor dewatering operations
Notes: The DEC permit we are talking about here is the excavation dewatering permit, not the CGP.

## Slide 42: ADEC Dewatering Permit AKG002000
Dewatering discharges eligible for coverage under this general permit consist of water pumped from excavation areas through the use of temporary dewatering wells or submersible pumps to lower the water table to support a construction activity. The dewatering of accumulated groundwater and storm water that accumulates within an excavation area is an authorized discharge under the permit. The permit does provide discharge authorization for dewatering conducted within 1,500 feet of a permit defined “DEC-identified contaminated site” although special permit conditions apply and additional requirements may be added in the discharge authorization. The special conditions will provide assurance that the dewatering activities does not pull contamination from known contaminated sites. See
http://dec.alaska.gov/water/wnpspc/stormwater/edhsgp.html

## Slide 43
Dewatering Notice Requirements
Submit an NOI and a certified BMP Plan to receive discharge authorization, IF
  1. You have excavation dewatering activities located within 1,500 feet of a permit defined “DEC-identified contaminated site,” or
  2. You have excavation dewatering activities located within 1,500 feet of a “contaminated groundwater plume” identified by Contaminated Sites, or
  You have excavation dewatering discharge to waters of the U.S. not
  covered by the Construction General Permit
IF answers to 1, 2, and 3 is No then no NOI Submittal is required. Projects not requiring an NOI still must comply with the conditions of the Excavation Dewatering General Permit. Dewatering discharge to the land is authorized in accordance to Part 4.0, Control Measures; Part 5.0, Monitoring Requirements; and Part 6.0, Reporting and Recordkeeping of the Excavation Dewatering General Permit.

## Slide 44
Dewatering may be difficult
But it’s not impossible!
What is Dewatering?
Notes: Dewatering is when we pump from a constructed excavation.

## Slide 45
Diversion
Notes: Diversions may be constructed and stabilized and not involve any dewatering.

## Slide 46
Pumped Diversion
Notes: Diversions can be pumped and not involve dewatering. This is simply putting the water that drains through the creek bottom cobble back in to the constructed diversion.

## Slide 47
Curb Appeal?
Notes: This is pumping from the excavation, this is excavation dewatering, note there is no perimeter control between the disturbed construction site and the flow.

## Slide 48
Diversion would intake here
We build it
We stabilize it
Notes: This intake location could be a diversion.

## Slide 49
This is Excavation Dewatering
Not a Diversion
Pump is drawing from the excavated area.
Flow is over constructed area
Notes: This is the upstream view. This water is running into the project from offsite.

## Slide 50
Dewatering
Soils Stabilization
Waterbody Protection Measures
Down Gradient Sediment Control
Consider the permit minimum measures
Notes: When inspecting always keep in mind the minimum measures we have gone over throughout the day.

## Slide 51
Have a Plan!
Write it down!
Modify if needed!

## Slide 52
Sitka
This plan must have
a lot of updates!
Notes: Sometimes you tell when things just don’t seem to be working out. There are 5 pumps in this picture.

## Slide 53
4.6 Treatment Chemicals
Requires:
Manufacturer MSDS Sheets
Trained employees
Site specific soil testing for treatability
4.6 2021 CGP

## Slide 54
What are the chemicals you will use?
Polyacrylamide
Chitosan
Include documentation:
MSDS Sheets
EPA approval for water use
Approval from CA, MN, OR, WA, WI for construction or AG
Non Toxic certification
Identify Operators & Training
Describe what chemicals will be used, including information required by CGP Section 4.6.2.3 Document the training for employees using treatment chemicals.
The SWPPP must:

## Slide 55
    Treatment chemical use procedures
Handling & Storage - Dose Rate - Mixing Requirements
Describe training for employees using treatment chemicals at the site. Document this training in SWPPP appendices.
The SWPPP must:

## Slide 56
Treatment Chemicals
For the purposes of this permit, means polymers, flocculants, or other chemicals used to reduce turbidity in storm water. Tackifiers and soil stabilizers (binders) are not considered treatment chemicals.
2021 CGP APP C

## Slide 57
    Project site conditions
Describe how proposed chemicals are suitable for use at the site.
Jar testing for treatability & dose rate
Mixing
Plan for sediment retention
The SWPPP must:

## Slide 58
    Application of treatment chemicals
The SWPPP must:
Briefly describe treatment chemical application procedures to be used.
How will it be used?
Petersburg

## Slide 59
  Active Treatment System information (CGP 4.6.7)
If the permittee plans to use cationic treatment chemicals or an active treatment system (as defined in Appendix C) they must submit a request to the Department fourteen (14) calendar days in advance of proposed usage.
Notes: The instructor could say that the Web site link is in the handout

## Slide 60
Application of Treatment Chemicals
Application of treatment chemicals through the use of manufactured products (e.g., gel bars, gel logs, floc blocks, etc.) must be used in combination with adequate ditch check dams, sediment traps, sediment basins, or physical control measure designed to settle out chemically treated storm water and minimize the presence of treatment chemicals before discharges reach waters of the U.S.
2021 CGP 4.6.5
Notes: This is to ensure we do not discharge sediment or chemical with the storm water.

## Slide 61
9. Good Housekeeping
Washing & Washout
Fueling & Maintenance
Fertilizer / Pesticides
Spill Prevention
Waste Handling

## Slide 62
Good Housekeeping
2021 CGP 4.8
A permittee must design, install, implement, and maintain effective good housekeeping measures to prevent and/or minimize the discharge of pollutants. A permittee must include appropriate measures for any of the following activities that are used at the site.

## Slide 63
    Washing of equipment and vehicles (CGP 4.8.1)
Prevent pollution to receiving areas
Wash water must be controlled
No detergent, soap or solvent
Notes: Discharge of solvent, soap, and detergents is prohibited. Oil and grease must be addressed as well.

## Slide 64
What will be washed?
Where will it be washed?
How will the discharge of pollutants be minimized?
Basin
Liner
Cap
Concrete
    Washout of applicators/containers used for paint, concrete, and other materials (4.8.4)
Notes: The reinforced plastic is being held on the dirt berm with more dirt. While not the most attractive this will work well. It could be improved by holding down the liner at the outside toe of the berm.

## Slide 65
Washout into steel “eco pan”
Clean entrance
No trackout
Document the good things that you notice
Juneau
Notes: Example of “eco pan” being used for concrete washout, clean entrance and streets. It’s important to reinforce good things. Noting positive observations is a good practice. Using safety meetings etc. as a way to let the crews know when there are good things in the field also will help in the overall site management.

## Slide 66
4.8.2 Fueling and Maintenance Areas
Designate areas to be used for fueling and/or maintenance of equipment and vehicles
Taylor Hwy

## Slide 67
4.8.2.4.3
Use drip pans or absorbents under or around leaky equipment and vehicles
Juneau

## Slide 68
Clean
Contained
Compliant

## Slide 69
4.8.3 Staging and Material Storage Areas
Designate areas that:
Minimize the exposure to precipitation and storm water and vandalism for all chemicals, treatment chemicals, liquid products, petroleum products, and other materials that have the potential to pose a threat to human health or the environment.
Goodnews Bay

## Slide 70
    Fertilizer or Pesticide use (CGP 4.8.5)
What will be used?
Where will it be used? + storage
When & how will it be used?
Follow the SWPPP & label requirements, minimize loss to runoff.
Notes: Products that could cause pollution in runoff must be stored and used in a manner that follows all regulations and does not pollute or harm the environment.

## Slide 71
4.8.6 Storage, Handling, & Disposal
of Construction Waste
Ft. Richardson
Provide for storage areas
Store Hazardous / toxic wastes in appropriate containers

## Slide 72
  Construction and Waste Materials (4.8.6)
The SWPPP must:
Describe in general terms the type of construction and waste materials expected to be stored at the site, with updates as appropriate, and describe the measures for handling and disposal of all wastes generated at the site, including clearing and demolition debris or other waste soils removed from the site, construction and domestic waste, hazardous or toxic waste, and sanitary waste.

## Slide 73
Be aware of spill reporting requirements in the SWPPP, SPCC, HMCP & DEC regulations.
  Spill notification (CGP 4.9)

## Slide 74
Secure from tipping
Stabilize surrounding areas
Provide clean service truck access
Juneau

## Slide 75
Any final questions?

## Slide 77: Evaluations help us improve AK-CESCL
Please take your time &
Include any comments