## Slide 1: CGP Good Housekeeping Requirements
Goals of this section:
Become familiar with the types of good housekeeping measures that are required by the CGP
Name on-site pollutants other than sediment
Know the steps required for winter shutdown
Know the what and who of BMP maintenance
Learn the names and functions of common good housekeeping BMPs
January 2022

## Slide 2
Prohibited Discharge
Wastewater from concrete washout, unless managed by an appropriate control measure;
Wastewater from washout and cleanout of stucco, paint, form release oils, curing compounds and other construction materials;
Fuels, oils, or other pollutants used in vehicle and equipment operation and maintenance; and
Soaps, solvents used in vehicle & equipment washing.
CGP Part 4.7 Pg. 31

## Slide 3
Good Housekeeping
A permittee must design, install, implement, and maintain effective good housekeeping measures to prevent and/or minimize the discharge of pollutants.
CGP Part 4.8 Pg. 32

## Slide 4
BMP
OR SC-11
AKDOT&PF – 42.00
The SWPPP must describe the pollution prevention measures used to eliminate or reduce non-storm water discharges.
Seattle
Washing of Equipment and Vehicles
& Wheel Wash-Down
CGP Part 4.8 1 Pg. 32
Notes: Stabilize entrance & parking areas with crushed rock to avoid trackout
Tire baths may be necessary in large construction jobs

## Slide 5
Automated Wheel Washing
Juneau

## Slide 6
Notes: Wash Water is Process Water
Note surface drainage back to wheel wash holding tanks for treatment.

## Slide 7: Dirty Wash Water Needs to Be Controlled Too
Juneau

## Slide 8
Fueling and Maintenance Areas
Designate areas to be used for fueling and/or maintenance of equipment and vehicles
Taylor Hwy
CGP Part 4.8.2 Pg. 32

## Slide 9
Locate such activities away from conveyance channels, storm drain inlets and waters of the U.S.;
Minimize the exposure to precipitation and storm water or use secondary containment structures designed to eliminate the potential for spills or leaked chemicals
Taylor Hwy

## Slide 10
Where & how will fuel be delivered, stored & managed.
Any prohibitions of practices?

## Slide 11
Be Prepared
Clean up spills or contaminated
surfaces immediately

## Slide 12
Good Housekeeping
The Never Ending Challenge.
Goodnews

## Slide 13
Be Prepared
Ensure adequate clean up supplies are available at all times to handle spills, leaks, and disposal of used liquids
Goodnews

## Slide 14
Use drip pans or absorbents under or around leaky equipment and vehicles
CGP Part 4.8.2.4.3 Pg. 33

## Slide 15
Staging and Material Storage Areas
Designate areas used for staging and material storage;
Locate activities away from storm water conveyance channels, storm water inlets, and WOUS; and
Minimize the exposure to precipitation and storm water and vandalism for all chemicals, treatment chemicals, liquid products, petroleum products, and other materials that have the potential to pose a threat to human health or the environment.
Goodnews Bay
CGP Part 4.8.3 Pg. 33

## Slide 16
Identify ways to reduce, stop, contain and clean up spills
Dispose of contaminated materials
Train personnel responsible for prevention and response
Fuel Tanks
Toilet
Equipment
Maintenance
Ketchikan
Notes: Construction sites may be subject to 40 CFR Part 112 regulations that require the preparation and implementation of a SPCC. If your site has a total storage capacity greater than 1,320 gallons and could discharge to navigable waters of the US your facility is subject to 40 CFR Part 112, your SWPPP should reference the SPCC Plan and keep the plan with the SWPPP.

## Slide 17
Washout of Applicators/Containers used
for Paint, Concrete, and Other Materials
Direct all concrete, paint, and washout activities into a lined, water-tight container or pit to ensure there is no discharge into the underlying soil and surrounding areas
Fairbanks
CGP Part 4.8.4 Pg. 33

## Slide 18
Tok

## Slide 19: Concrete Slurry is a Pollutant
Concrete Slurry From Pouring & Sawcutting Pollutes Stormwater With High pH
Do Not Allow Slurry to Mix With Stormwater
If Slurry Mixes With Stormwater Then Treat With Dry Ice or CO2 Sparging
Concrete Clean Up Should Be Done Only in Formed Areas
Unused Concrete Should Be Returned for Recycling

## Slide 21
Concrete Handling
Concrete contributes turbidity and High pH
Return unused concrete to plant
Wash chutes, pumps, hand tools into a contained area
BMP
WA C-151
OR NS-14
AKDOT&PF-06.00
Notes: Includes the finishing tools. Note the pump truck is using no containment. Make sure the containment liner is sufficient for the volume.

## Slide 22
Designate areas to be used for washout

## Slide 23
Notes: Video: Concrete washout

## Slide 24
For concrete washout areas, remove hardened concrete waste when it has reached ½ the height of the container or pit
Goodnews
Village Concrete Washout
CGP Part 4.8.4.5 Pg. 33

## Slide 25
Storage, Handling, & Disposal
of Construction Waste
Ft. Richardson
Provide for storage areas
Store Hazardous / toxic wastes in appropriate containers
CGP Part 4.8.6 Pg. 33

## Slide 26
Haz-Mat Storage
Petersburg

## Slide 27
Why is it here?

## Slide 28
Prevent discharges of pollutants to the drainage system or receiving water. Clean and inspect regularly for leaks and spills.
Provide containment of portable toilets
Kotzebue
Secondary Containment
Rope tie downs
CGP Part 4.8.6.4 Pg. 34

## Slide 29
Stuck between rocks & a smelly spot!

## Slide 30
Photo Courtesy WADOE modified
Porta Potty Pollution Prevention Plan
Pee Pee PPP
Notes: Or a PP PPP for short.

## Slide 31
Notes: Video Clip “Oh Crap 2 for module 2”

## Slide 32: Spill Notification
A permittee is prohibited from discharging hazardous substances or oil from a spill or other release. Alaska state law (18 AAC 75.300) requires all oil and hazardous substance release be reported to DEC Spill Prevention and Response program. Spill reporting placards can be found at the following webpage: https://dec.alaska.gov/spar/ppr/spill-information/reporting
To report a spill, call the nearest DEC Area Response Team Office:
  Southeast (Juneau) – 465-5340
  Central (Anchorage) – 269-3063
  Northern (Fairbanks) – 451-2121
Outside of normal business hours, the permittee must call (800) 478-9300 to report the spill as soon as the permittee has knowledge of the discharge
CGP Part 4.9 Pg. 32

## Slide 33
Secondary Containment With Notice

## Slide 34
Understand & Follow
All Reporting Requirements
Even if Spills are into
Contained areas
> 55 Gallons = 48 Hours
Report all Spills Between
1 & 10 Gallons Monthly
To Water any amount
Report Immediately
Hazardous, Any Amount
Report Immediately
OIL SPILLS

## Slide 35: Permanent Storm Water Management Control
A permittee who constructs, alters, installs, modifies, or operates any part of a permanent storm water management control at a site must submit a copy of the engineering plans for review.
North Pole
CGP Part 4.11 Pg. 34

## Slide 36: Winter Shutdown
The permittee must identify the anticipated dates of fall freeze-up and spring thaw for their site and plan for winter shutdown.
Frozen ground by itself is not considered stabilization.
A permittee must provide for :
Stabilization of conveyance channels; disturbed slopes, disturbed soils, and soil stockpiles.
Erosion and sediment control measures in anticipation of spring thaw.
CGP Part 4.12 Pg. 34

## Slide 37
Winter Construction
Permit coverage is not required for the construction of ice roads or the placement of sand or gravel on frozen tundra with no excavation or potential to pollute waters of the U.S.
CGP Part 4.12.2 Pg. 35

## Slide 38: Maintain BMPs
All BMP’S Have Designed Performance Goals & Standards
All BMPs Should Have the Performance Goals Detailed in the SWPPP
CGP Part 4.13 Pg. 35
Notes: BMPs must be continually maintained – especially after rain events

## Slide 39
A permittee must maintain all control measures, good housekeeping measures, and other protective measures in effective operating condition.
CGP Part 4.13.1 Pg. 35

## Slide 40
If site inspections required by Part 6.0 identify control measures, good housekeeping measures, or other protective measures that are not operating effectively, the permittee must implement corrective actions in accordance with Part 8.0.
Ketchikan
CGP Part 4.13.1 Pg. 35

## Slide 41
If existing control measures need to be modified or if additional control measures are necessary for any reason, the permittee must complete any corrective action in accordance with Part 8.2.
CGP Part 4.13.2 Pg. 35

## Slide 42
A permittee must remove sediment from silt fences, check dams, berms or other controls before the accumulated sediment reaches:
One-third (⅓) the distance up the above-ground height (or it reaches a lower height based on manufacturer’s specifications) for silt fences;
One-half (½) the distance up the above-ground height (or it reaches a lower height based on manufacturer’s specifications or BMP guidance manuals) for storm water inlets, check dams, berms, or other control measure; or
For sediment traps or sediment ponds, the permittee must remove accumulated sediment when the design capacity has been reduced by fifty (50%) percent.
Anchorage
CGP Part 4.13 Pg. 35

## Slide 43: MAINTAIN BMPs
All BMPs require maintenance
Proper installation is only the first step
Inspect on a regular basis and after every discharge
Designate a person to inspect E & S controls
Notes: All erosion and sediment control BMPs require regular maintenance to function. Proper installation alone is no guarantee of success. They should be inspected on a regular basis and after every storm event. Frequent occurrences include storm drain inlets becoming clogged, silt fence overwhelmed by runoff and sediment after a storm, sediment traps filling in and stabilized construction entrances sinking into the mud. These devices are useless in poor condition. We highly recommend designating someone to visually inspect E&S controls every day, reporting back to the construction manager with recommendations for maintenance or replacement.

## Slide 44
Maintenance of Controls
Summarize routine maintenance of BMPs.
Include schedules (daily, weekly, etc.) as well as who is responsible.
Detail maintenance procedures for individual BMPs.
All maintenance activities must be documented.
Use corrective action log to describe all maintenance.
Notes: For more on this topic, see SWPPP Guide, Chapters 4 and 5 and the suggestions on the Sample Inspection Report in Appendix B.

## Slide 45
BMP’s Need More Than “On The Fly” Maintenance

## Slide 46: Some BMPs in Certain Situations are Harder to Maintain Than Others

## Slide 47: Timely Monitoring of BMPs is Required and prudent
Responsible Person (AK-CESCL) Must Inspect & Record BMP Performance
BMP Performance Must be Inspected per all Permit Conditions
Schedule must be in the SWPPP

## Slide 48: BMP Inspections
Qualified Inspectors Must Fill Out Inspection Checklists/Reports
You Must Record BMP Maintenance
You Must Record any Sampling Data of Stormwater Discharge

## Slide 49
How do you do what you do?
Are your means and methods compliant with all permit conditions?
Notes: Ask your self with regards to all tasks associated with your project.

## Slide 50
Debris Bins
Covered Soils
Inlet Protection
Gravel Entrance
Driveway Perimeter Control
Clean Streets
Notes: Clean & Tidy

## Slide 51: Debris Free Zone: Clean Access for Clients & Crew

## Slide 52
Innovative thinking, Risk Management
Notes: Place Matting Materials Down Where People Walk

## Slide 53
Temporary “Winter Over” Erosion Control
Pre-Load Pile
Wattles
Site Outlet
Pipe Drain
Jute Lined
V- Ditch

## Slide 54
Stockpile Covered
Stockpile Silt Fence
  Reinforced for Flow (Straw Bales)
Lot Grading Perimeter Silt Fence
Buffer Zone
Wire Backed Silt Fence at Site Perimeter

## Slide 55
Notes: Step by step implementation

## Slide 56
Sediment Controls must be removed
30 days after final site stabilization
Notes: Someone has to remove the BMP’s for permit compliance.

## Slide 57
Cutting Edge
BMP Removal
Strategies
Free Acquisition
Of Materials
Be on the lookout for
Cost Saving Opportunities

## Slide 58
Stabilized Site
Scheduling
BMP
WA C-162
OR EP-1
Bonneville Dam
Notes: Scheduling and manage the project are the best BMP’s for construction activities.

## Slide 59: MANAGE THE PROJECT
Notes: The approved Sediment and Stormwater plans must be kept on site, accessible, and must be referred to frequently. The plan should be strictly adhered to with particular attention paid to the sequence of construction. Any deviations need to be approved by the review agency. Certain changes require formal revisions to the Sediment and Stormwater plans. Coordinate with utilities and subcontractors to minimize conflicts and impacts on erosion and sediment controls. Project managers should have equipment and materials available for stabilization, dust control, street sweeping and BMP maintenance. For example, ordering additional stone will permit regular maintenance of the stabilized construction entrance without having to wait for availability. An open dialog should be maintained with the project owner, engineer, E&S control material suppliers, inspector and delegated agency representative. It is beneficial to include erosion and sediment control aspects of the project in any progress meetings.

## Slide 60
Doing It Right Won’t Kill You !